## Slide 1
삼성 DS2과정 프로젝트
Image Restoration Challenge
Jongho Lee, Ph.D
Laboratory for Imaging Science and Technology
Department of Electrical and Computer Engineering
Seoul National University

## Slide 2
Physics informed neural network

## Slide 7
Why do we care?

## Slide 8
Generalization issues in deep learning

## Slide 9
Suscep map
Local field map
Deconvolution
=
Convolution
Dipole
Local field distr
-1
=
Dipole
Suscep distr
Susceptibility map is generated from local field map by dipole deconvolution
Fourier transform suggests dipole deconvolution requires division by zeros
Dipole deconvolution

## Slide 10
Multiple head orientation data
  Remove zeros using three or more orientation data (COSMOS)
Single head orientation data
  k-space threshold (TKD), regularization using magnitude edge information (MEDI) and others (iLSQR, HEIDI, ….)
Tian Liu, MRM 2009
Sam Wharton, MRM 2010
Ludovic de Rochefort MRM 2008
Karin Shmueli, MRM 2009
Tian Liu, MRM 2011
Christian Langkammer, NeuroImage 2012
Wei Liu, NeuroImage 2015
Practical
Contain errors
Gold standard
Not practical
Dipole deconvolution

## Slide 11
Dipole deconvolution using deep learning
Neural network shown success in inverse problem when expensive gold standard label is available e.g., parallel imaging with full sample data, low dose CT with full dose data
In QSM: for training, expensive COSMOS as label paired with single orientation local field as input
for inference, single orientation local field as input, generating COSMOS-quality QSM map
McCann, IEEE SPM 2017
Wang, Nature MI 2020
high cost data
QSMnet Yoon, NeuroImage 2018
DeepQSM Bollmann, NeuroImage 2019

## Slide 12
QSMnet
COSMOS
TKD
MEDI
Yoon, NeuroImage 2018
3D U-net
Streaking free maps
Computational efficiency (few secs)
COSMOS-trained or simulation-trained
Dipole deconvolution using deep learning
Jung, NMR BioMed 2020

## Slide 13
Dipole deconvolution using deep learning
QSMGAN: GAN improves quality
QSM outside of brain with fat
AutoQSM: No need for background removal
or brain mask
Wei, NeuroImage 2019
Chen, NeuroImage 2020
Hanspach, MRM2022
Recovering SWI-filtered phase data
Kames, MRM 2022
SWI-filtered phase Recovered Original

## Slide 14
Dipole deconvolution using deep learning
FINE: Self transfer learning with physical model loss
VaNDI: Combine nonlinear dipole inversion
with variational network
MoDL-QSM: Physics model enforced with
network as regularizer
Generalization to untrained input
Zhang, Neuroimage 2020
Polak,
NMR Biomed
2020
xQSM: Octave conv and noise-regularization
Generalization for resolution
Gao, NMR Biomed 2021
Feng, Neuroimage 2021

## Slide 15
  Issues of “generalization”
  Issues of “performance comparison”
  Issues of “performance”
Issues with deep learning dipole deconvolution

## Slide 16
  Issues of “generalization”
  Issues of “performance comparison”
  Issues of “performance”
Issues with deep learning dipole deconvolution

## Slide 17
• QSMnet
• QSMnet+
Training data distribution of QSMnet
Susceptibility value in lesion
Conventional QSM (ppm)
QSMnet (ppm)
Number of voxels
Susceptibility value (ppm)
Hemorrhage
Jung, NeuroImage 2020
Generalization: Susceptibility range
QSMnet was trained with limited susceptibility range (-0.4 to 0.6 ppm)
Hemorrhage with high susceptibility (>1 ppm) was underestimated in QSMnet
Augmentation using simulated data improves hemorrhage estimation in QSMnet+

## Slide 18
Jung, NMR BioMed 2020
Lower resolution
Higher resolution
Generalization: Resolution

## Slide 19
Oh, Med Img Anal 2022
Generalization: Resolution
Gao, NMR Biomed 2021
Unsuprevised learning with adaptive instance normalization

## Slide 20
Generalization: Resolution
Sooyeon Ji
QSM workshop 2022
1 x 1 x 3 mm3 data inference for network trained using 1.5 mm iso

## Slide 21
Performance of deep learning QSM changes if test data has different characteristics from training data
Høy, ISMRM2019
Jung, NMR BioMed 2020
Generalization
Notes: Then, the linearity was improved in the new version of QSMnet, named as QSMnet+
This work was presented on last Monday with the number of abstract 317.

## Slide 22
Generalization: Solutions using network architectures
FINE: Self transfer learning with physical model loss
VaNDI: Combine nonlinear dipole inversion with
variational network
MoDL-QSM: Physics model enforced with
network as regularizer
Generalization to untrained input
Feng, Neuroimage 2021
Zhang, Neuroimage 2020
Polak, NMR Biomed 2020
Networks need to be explored for generalization capability

## Slide 23
  Issues of “generalization”
  Issues of “performance comparison”
  Issues of “performance”
Issues with deep learning dipole deconvolution

## Slide 24
Performance comparison
No large size "public" dataset available for QSM
Comparison via "private" data of different characteristics (resolution, background removal ...)
Chungseok Oh
Comparison with pre-trained net not fair due to data characteristic difference affecting performance
Comparison with re-trained net not fair because retrain net is no longer the same as original net
Notes: First, as we explained previous slide,
The training data of QSMnet consists of healthy subjects.
The training data distribution of QSMnet is plotted as shown here.
The x-axis is the susceptibility value of the voxel in training images, and y-axis is the number of voxels.
Since the network never observed the large susceptibility values such as hemorrhage lesions, or calcification during training stage,
we don’t know the network can perform properly in this range.

## Slide 25
Performance comparison - reproducibility
Deep neural network has shown limited reproducibility
For fair comparison, use of public dataset and sharing pretrained network is recommended
Renard, Sci Rep 2020 Alahmari, IEEE Acess 2020
Oh, ISMRM 2022
QSMnet and variational network
Metrics: SSIM, RSME
For training, CUDA convolution bench marking and determinism, mini-batch order, and network weight initiation affect results
For inference, mostly reproduciblity
Notes: First, as we explained previous slide,
The training data of QSMnet consists of healthy subjects.
The training data distribution of QSMnet is plotted as shown here.
The x-axis is the susceptibility value of the voxel in training images, and y-axis is the number of voxels.
Since the network never observed the large susceptibility values such as hemorrhage lesions, or calcification during training stage,
we don’t know the network can perform properly in this range.

## Slide 26
  Issues of “generalization”
  Issues of “performance comparison”
  Issues of “performance”
Issues with deep learning dipole deconvolution

## Slide 27
Performance
Meaning of better performance?
Still problem of generalization? (7T? unbalanced training for high iron concentration?)
Can we design network for improved performance for deep gray matter iron quantification?
Yao, NI clinical available online
Deep learning shown high quality results but conventional recon outperformed in challenge 2.0
QSM Challenge, MRM 2021
Redefine performance matrix (not only SSIM but "functional" performance)

## Slide 28
Generalization vs. Harmonization

## Slide 29
Generalization vs. Harmonization
Siemens
Philips
Generalization:
  Develop neural network that can process various conditions of input
  (e.g., different vendor images)
Harmonization:
  Process input image to have similar characteristics to training data
Cons and pros:
  Need more data or new design
  May generalize for unknown domain
  Takes longer time for training
*No need to worry if network is used for the same characteristic dataset as train data
How:
  Preprocessing using neural network
How:
  Data augmentation, network architecture
Cons and pros:
  Need to design new network (require data)
  Takes longer time for inference

## Slide 30
Siemens
Philips

## Slide 31
Image harmonization: Style transfer
0.43 x 0.43 x 1.5 mm3
If paired data set available: Supervised learning
Only unpaired data available: Style transfer via cycleGAN
Combine both for limited paired data
Isola, CVPR 2017
CycleGAN
Siemens
(unpaired)
Philips style image
Philips
Philips style
or not
fake
real
Siemens
(pair A)
Philips style image
Siemens
(pair A)
Philips
(pair A)
Siemens
(pair A)
Philips style
or not
fake
real
CycleGan with paired data
Zhu, ICCV 2017

## Slide 32
Image harmonization: Style transfer
0.43 x 0.43 x 1.5 mm3
Joonhyeok Yoon
ISMRM 2022